## Slide 1
august 8-10, 2017| cape neddick, me
Andrew Gillespie
(413) 540-4088
agillespie@iso-ne.com
Zonal Demand Curves: CSO Transactions using MRI Demand Curves

## Slide 2
Zonal Demand Curves: CSO Transactions using MRI Demand Curves
WMPP ID:
103
Proposed Effective Date: ARA1 for Capacity Commitment Period 11
The current annual CSO Bilateral construct is incompatible with the use of zonal Marginal Reliability Impact (MRI) demand curves in annual reconfiguration auctions
This presentation will:
  Review Annual Reconfiguration Transactions (ARTs)
  Describe the conforming changes included with this proposal as they relate to:
    Monthly CSO Bilaterals and reconfiguration auctions
    Significant decrease thresholds and ‘mandatory’ demand bids in ARA3
    Annual and Seasonal CSO Bilaterals
At the next meeting we will review the Tariff changes and the Financial Assurance Policy changes (to be coordinated with the Budget & Finance Subcommittee)

## Slide 3: Problem Summary
The problem: The current annual CSO Bilateral construct is incompatible with the use of zonal Marginal Reliability Impact (MRI) demand curves in annual reconfiguration auctions
The substitutability of capacity across constrained zone boundaries is now variable (not kW-for-kW)
CSO Bilaterals work only when the capacity being transferred is fully substitutable (kW-for-kW)

## Slide 4: Proposal
The solution: Replace annual CSO Bilaterals with Annual Reconfiguration Transactions (ARTs)
This new mechanism assesses the impact of transfers rather than requiring a precise ratio for each transfer to avoid any impact
ARTs have simple terms, provide more utility to participants, and are vastly simpler to administer

## Slide 5: Today’s Topics
Background & Review: Provide a brief recap of previous presentations describing the Annual Reconfiguration Transaction mechanism
Conforming changes: Explain and discuss the associated conforming changes
Implementation: Discuss when the ART proposal can be implemented and possible temporary solutions
Tariff changes: Review the scope of the Tariff changes associated with this proposal and the various committees involved
Questions: Review questions and comments from prior meeting

## Slide 6: Previous presentations – A quick review

## Slide 7: CSO Substitutability
For Capacity Commitment Periods (CCPs) through CCP 10
Fixed zone demand parameters were used, which relied on transfers being either:
  Fully substitutable (kW-for-kW), or
  Not allowed if it would violate the fixed demand requirement
Beginning with CCP 11, MRI-based zone demand curves are used
CSO transfers are allowed across zone boundaries at all points; there are no fixed requirements to prohibit transfers
Capacity is now substitutable at all points; but the substitution is not kW-for-kW at all points

## Slide 8: How to Facilitate ‘Private’ Transfers?
  The advantage of a ‘private’ transfer versus the annual reconfiguration auction (ARA) is price certainty
  Participant A: What price can I shed this CSO?
  Participant B: What price can I acquire a CSO?
If we ignore partial substitutability, there is no accounting for the reliability impact on the system
  If it improves, consumers are advantaged at suppliers’ expense
  If it worsens, suppliers are advantaged at consumers’ expense
A mechanism is needed that:
  Provides price certainty for annual CSO transfers, and
  Accounts for the impact on the system

## Slide 9: Proposal: Annual Reconfiguration Transaction (ART)
What is it?
  An agreement that achieves the equivalent of a fixed price ‘private’ transfer, based on the intent of one participant to shed a resource’s CSO in the ARA and the intent of another participant to acquire a CSO in the ARA
The parties negotiate and agree on the following ART terms:
  The specific transferring and acquiring resources
  The transaction amount (MW)
  A set price ($/kW-mo.) and capacity zone
Separately, participants submit demand bids and supply offers into the ARA for the specified transferring and acquiring resources

## Slide 10: How Does an ART Work?
The ISO settles payments involving the transferring resource and the acquiring resource
The payment amount: ART amount (MW) x (Zone ARA clearing price – set price) (+/-)
  If positive, the transferring party receives a payment and the acquiring party makes a payment
  If negative, the transferring party makes a payment and the acquiring party receives a payment

## Slide 11: ART Summary
Annual Reconfiguration Transactions:
Allow for exchanges where they were previously prohibited, and can accommodate both uneven transfers and kW-for-kW exchanges
This is possible because they account for the impact of capacity transfer across constrained zone boundaries
This mechanism can be used for transfers in the same zone, or across constrained zone boundaries
  Using both an ART and a bid (or offer) provides price-quantity assurance
This mechanism meets our objectives; find a means to:
  Provide price certainty for annual CSO transfers, and
  Account for the effect of partial substitutability on reliability (i.e., resource adequacy)

## Slide 12: Other ART Observations
ARTs have simple terms to negotiate
  Which two resources, how much, what price, and where?
ARTs work when the clearing price is not a function of the marginal reliability impact
  E.g., the transition (flat) segment of the system demand curve
ARTs do not require a precise ratio or exchange rate
  The ART amount may be different than the demand bid and supply offer amounts
    E.g., a 9.964 MW shedding resource and a 10.164 MW acquiring resource could use a 10 MW ART; a CSO Bilateral would be limited to 9.964 MW
ARTs do not require any separate processing
  Reliability reviews are done on the demand bids and supply offers only

## Slide 13: Differences Between ARTs and CSO Bilaterals
ARTs will be submitted at the same time demand bids and supply offers are submitted for the ARA
  No separate process or schedule for ARTs
ARTs are only to be used when a demand bid or supply offer is submitted in the ARA
Similar to demand bids in the ARA, financial assurance will be assessed for ARTs
  Failing financial assurance requirements will result in a participant’s ARTs being cancelled

## Slide 14: Limits and Reliability Reviews
The ART amount may be different than both the demand bid and supply offer amounts, but must be less than the maximum qualified bid/offer amount of the two resources
  Example on next slide (per request from last meeting)
A MW from a resource associated with an ART cannot be used in any other (subsequent) ART (for that ARA)
The ART will be cancelled if either the demand bid or supply offer is denied during the auction for reliability reasons
Withdrawing an ART before, or cancelling an ART during the auction will not result in the withdrawal or cancellation of demand bids or supply offers

## Slide 15: ART Limit - Example
An ART between Resource A and Resource B would be limited to 110 MW
This ‘higher-of’ limit allows for the use of a ‘ratio’ while also limiting ARTs to the maximum possible participation in the ARA
  You can’t enter an ART if you can’t participate in the ARA
Also, there can’t be more than one ART on a MW
  In this example, a 110 MW ART would ‘use up’ each resource’s ART eligibility
Before each ARA every resource has a maximum demand bid and maximum supply offer limit
Resource A
  Maximum Demand Bid = 90 MW
  Maximum Supply Offer = 0 MW
Resource B
  Maximum Demand Bid = 0 MW
  Maximum Supply Offer = 110 MW

## Slide 16: conforming changes for annual reconfiguration transactions
Monthly CSO Bilaterals and reconfiguration auctions
Significant decrease thresholds and ‘mandatory’ demand bids in ARA3
Annual and Seasonal CSO Bilaterals

## Slide 17: Monthly CSO Bilaterals and reconfiguration auctions
Monthly demand parameters; what fixed requirements will be used in monthly CSO Bilaterals and reconfiguration auctions?

## Slide 18: Monthly CSO Bilaterals
Recall: The ISO will continue to use fixed demand requirements in the monthly reconfiguration auctions
  There exists no MRI-based demand curves of a monthly frequency
CSO Bilaterals depend on modeling constrained zone boundaries as fixed demand requirements, meaning transfers are either:
  Fully substitutable (kW-for-kW), or
  Not allowed if it would violate the fixed demand requirement
Problem: Continuing to use the Local Sourcing Requirement (LSR) and the Maximum Capacity Limit (MCL) in the monthlies (beginning with CCP 11) would ignore partial substitutability
  E.g., an import-constrained zone transfer below (to the left of) the zonal MRI curve truncation point but above (to the right of) LSR would ignore the fact that substitutability is not kW-for-kW in this range (see chart on next slide)

## Slide 19: Substitutability Comparison
CCP 11 +
CCP 9 & 10
CCP 8

## Slide 20: Proposal: Use MRI Truncation Points
Beginning with June 2020 (the first month of CCP 11), use the annual MRI-based demand curve truncation point as the zonal fixed requirement for both monthly CSO Bilaterals and reconfiguration auctions
The truncation point being where the zonal MRI-based demand curve price is zero
Forward Capacity Auction 11 |  |  | 
 | LSR/MCL | Truncation point | Total CSO in zone after FCA
SENE | 9,907 | 10,538 | 11,736
NNE | 9,000 | 8,510 | 8,344

## Slide 21: Significant decrease thresholds and ‘mandatory’ demand bids in ARA3
A review of the significant decrease thresholds and the use of ‘mandatory’ demand bids in ARA3

## Slide 22: Scope
As part of the ART proposal, the ISO is proposing to modify:
The consequences of a capacity deficiency prior to ARA3 Whether because of a significant decrease or a resource that may not be ‘commercial’ - under what conditions should a resource be forced to have a demand bid in ARA3?
How a significant decrease is determined What constitutes a ‘significant’ decrease?
There are no proposed changes to how a resource is qualified

## Slide 23: Significant Decreases - Background
The ISO conducts two significant decrease checks
During FCA qualification
  When qualifying resources for participation in the FCA an observed significant decrease may result in a lower qualified amount
  How much of a CSO in the FCA should you be eligible for, given the capability deficiency the ISO has observed prior to the FCA?
During ARA3 qualification
  When checking each resource’s capability prior to ARA3 an observed significant decrease may result in the resource being forced to ‘cover’
  Now that you have a CSO, how much of that can you keep given the capability deficiency the ISO has observed prior to ARA3?

## Slide 24: Roadmap:
First, we will examine the qualification of resources prior to ARA3
From our observations we will then build-up the proposed changes applicable to:
The significant decrease provisions, as they apply to both ARA3 and the FCA
When and how the ISO would, on behalf of a participant, submit a demand bid for a resource in ARA3

## Slide 25: ARA3 Resource Qualification
Each October the ISO qualifies resources for ARA3
  Each resource’s Qualified Capacity values (summer and winter) are determined based on the most recent seasonal data available
For each month of the commitment period a deficiency is calculated; CSO – Qualified Capacity > 0?
Is that deficiency a material problem?
If a participant does not somehow address an identified material problem prior to ARA3, the ISO will submit on behalf of the participant a demand bid for the resource in ARA3 to cover the deficiency

## Slide 26: ARA3 Qualification - Outcomes
There are three general outcomes:
All is good. Based on a resource’s latest audit values or the latest construction schedule update, it appears the resource will be capable of meeting its CSO in every month of the commitment period
There is an abnormality. Based on audit values or the latest construction schedule update, it appears the resource will be capable of meeting its CSO in only some months of the commitment period
There is a problem. Based on audit values or the latest construction schedule update, it appears the resource will be incapable of meeting its CSO in any month of the commitment period

## Slide 27: Observation #1: Timing of ARA3 Qualification
ARA3 qualification is done in the fall and is a lagging indicator
The qualification of capacity resources is done approximately seven months prior to the start of the commitment period
Qualification is based on the most recent seasonal data on record (i.e., data on record from audit periods that occurred at least seven months prior to the start of the commitment period)

## Slide 28: Observation #1: Timing of ARA3 Qualification False Positives
An ‘all is good’ determination may be a false positive
Because qualification is done several months before the beginning of the commitment period, and is based on observations made prior to that time (perhaps several months prior), this determination is not a guarantee that a resource will actually be capable of meeting its CSO in every month of the commitment period
E.g., A resource may suffer a catastrophic and unrepairable failure the day after completing a satisfactory seasonal audit that is used in ARA3 qualification

## Slide 29: Observation #1: Timing of ARA3 Qualification False Negatives
A ‘problem’ or ‘abnormality’ may be repairable or explained (i.e., it was a false negative)
For year-round problems, ARA3 qualification provides better evidence that there is a real and persistent problem
  The resource has both summer and winter audits that, when compared to the resource’s CSO each month, appear to indicate that the resource will be incapable of meeting its CSO (or at least a material portion of it) in any month of the commitment period
However, for abnormalities the evidence is less compelling; we can’t really tell if the situation is a real abnormality or:
  A year-round problem, but only reflected in one seasonal audit?
  A repairable situation; perhaps it was just a bad seasonal audit?

## Slide 30: Observation #1: Timing of ARA3 Qualification Takeaways
It is very difficult to accurately, objectively, and with absolute certainty determine before the commitment period begins, whether or not a given resource will be capable of delivering on its CSO over the entire commitment period
In all cases, there are Pay-for-Performance (PFP) consequences when a resource fails to deliver on its CSO Whether a resource:
  Suffers a significant decrease after ARA3 qualification,
  Submitted a restoration plan that didn’t work,
  Indicated the resource was going to be commercial before the start of the commitment period but failed to do so, or
  Suffers a forced outage a few days into the commitment period,
  The consequences for failing to deliver are the same

## Slide 31: Significant Decrease Thresholds After ARA3 Qualification
For each resource a deficiency is calculated (for each month)
  Deficiency = CSO – Qualified Capacity > 0?
Currently, a deficiency is deemed ‘significant’ if it exceeds 20% of the resource’s CSO or 40 MW, whichever is lower
For resources with a CSO > 200 MW, the 40 MW threshold applies
  E.g., A resource with a 300 MW CSO could have a 35 MW decrease and the current thresholds will not flag the deficiency as ‘significant’
For resources with a CSO < 200 MW, the 20% threshold applies
  E.g., A 3 MW resource could have a 1 MW decrease and this provision will flag the deficiency as ‘significant’

## Slide 32: Observation #2: Significant Decrease Thresholds Some Examples (ARA3)
CSO | Deficiency | Current Significant Decrease Parameters | 
 |  | Limit | Significant?
250.0 | 38.0 | 40.0 | No
50.0 | 6.3 | 10.0 | No
25.0 | 3.1 | 5.0 | No
10.0 | 1.3 | 2.0 | No
5.1 | 1.1 | 1.0 | Yes
1.1 | 0.231 | 0.220 | Yes
Each line in the table is an example of how a resource with a given CSO and deficiency would be evaluated
Deficiency = CSO - QC
In each case using the current thresholds, is the deficiency deemed a significant decrease?

## Slide 33: Observation #2: Significant Decrease Thresholds Actual Occurrences (ARA3)
CSO | Average Number Observed | Average Total Amount (MW)
< 2 MW | 219 | 104.4
2 – 10 MW | 57 | 249.3
10 – 40 MW | 16 | 295.0
> 40 MW | 3 | 265.4
Total | 295 | 914.1
For each CCP there was, on average:
708 resources
33,525 MW of CSO
For each ARA3 there was, on average:
295 resources identified as having a significant decrease (41% of the entire fleet!)
From those 295 resources, 914 MW was identified as being a significant decrease (< 3% of the total CSO)
This data is based on actual determinations made in the last three ARA3s (for CCPs 6, 7 & 8)

## Slide 34: Observation #2: Significant Decrease Thresholds Takeaways
The current significant decrease thresholds produce an outcome that focuses on the relatively small deficiencies
The smaller the CSO the more likely a relatively minor deficiency in magnitude will result in a significant decrease – however small
The larger the CSO the more likely a relatively major deficiency in magnitude will not result in a significant decrease

## Slide 35: Maximum Bid/Offer Amounts in ARAs
There are limits to what a participant can bid or offer in annual reconfiguration auctions (to keep things ‘physical’):
Supply offers are limited to the resource’s minimum (unsubscribed) Qualified Capacity (QC) rating; The largest supply offer allowed is set by the month that has the combination of the lowest qualified capacity rating, less any CSO amount You can’t acquire a CSO amount in any month that is greater than the resource’s QC amount that month
Demand bids are limited to the resource’s minimum CSO amount; The largest demand bid allowed is set by the month that has the lowest CSO You can’t shed a CSO amount in any month that is greater than the resource’s actual CSO amount that month – no negative CSO

## Slide 36: Maximum Demand Bid Amount - Example
Consider a resource with a CSO of 6 MW in the summer and 10 MW in the winter (top picture)
The most a participant would be able to submit for this resource in an ARA is a 6 MW demand bid (middle picture)
If a 10 MW demand bid were allowed, the resource would end up with a negative 4 MW CSO in the some months; 6 MW – 10 MW = (4) MW (bottom picture)

## Slide 37: ‘Mandatory’ Demand Bids in ARA3
The ISO will submit on behalf of a participant a demand bid for a resource in ARA3 if:
There is an unresolved significant decrease
The participant reports that the resource will not be ‘commercial’ before June 1
The MW quantity of this mandatory annual demand bid is set by the worst affected month
This approach is inconsistent with participant demand bid limits, and has two notable consequences:
It can overcorrect
It may create a negative CSO

## Slide 38: Overcorrection
Consider a resource with a 10 MW CSO in all months
The resource’s ARA3 Qualified Capacity is 8 MW in the summer and 3 MW in the winter (top picture)
The maximum deficiency is in the winter and is a significant decrease; a 7 MW mandatory demand bid is submitted in ARA3 (middle picture)
Because of the winter problem the resource is stripped of its CSO in the summer, while at the same time remaining qualified in the summer (bottom picture)

## Slide 39: Overcorrection - Takeaways
As a consequence of an abnormality in some months, a resource may be stripped of a CSO in other unaffected months, while remaining qualified in those months (have a higher QC than CSO)
A resource is not required to re-acquire a CSO in the overcorrected months
  Based on the specific months effected, monthly CSO prices, and a participant’s expectation of scarcity conditions under PFP, a participant may decide to avoid a CSO in some overcorrected months

## Slide 40: Negative CSO
Consider a resource with a 4 MW CSO in the summer and 10 MW in the winter
The resource’s Qualified Capacity is 3 MW in all months (top picture)
The maximum deficiency is in the winter and is a significant decrease; a 7 MW mandatory demand bid is submitted in ARA3 (middle picture)
Because of the winter problem the resource now has a negative CSO in the summer (bottom picture)

## Slide 41: Negative CSO - Takeaways
In the months when the CSO is negative the participant would be charged (positive CSOs get paid)
During a scarcity condition a negative CSO would create a positive performance score, even if the resource failed to provide any energy or reserves
During scarcity conditions, the balancing ratio for PFP would include this negative CSO

## Slide 42: Mandatory Demand Bids in ARA3 Takeaways
The consequences of an overcorrection may be a benefit or harm to the participant, and is a consequence that has nothing to do with the significant decrease ‘problem’ months
The consequences of a negative CSO are bizarre and inconsistent with the limits placed on participant-submitted demand bids

## Slide 43: Summary of Observations and Takeaways
The data used to determine if there is a problem prior to ARA3 is not an absolute predictor, and is subject to false positives and false negatives
  But, whether or not a resource has been identified as having a problem before ARA3, there are Pay-for-Performance (PFP) consequences when a resource fails to deliver on its CSO
The current significant decrease thresholds produce an outcome that focuses on relatively small deficiencies
Mandatory demand bids for abnormalities (part-year deficiencies):
  May overcorrect
  May create a negative CSO
  Are inconsistent with limits on participant-submitted demand bids

## Slide 44: Proposal
The consequences of a capacity deficiency prior to ARA3
  Modify the ISO’s use of mandatory demand bids such that:
  Their use would not overcorrect in other months; i.e., mandatory demand bids would not be used to address an abnormality
  Their use is consistent with participant allowable limits; a mandatory demand bid would not result in a negative CSO; i.e., base any mandatory demand bid quantity on the least effected month
How a significant decrease is determined
  Modify the significant decrease thresholds used to identify whether or not a monthly deficiency is a material significant decrease
  Use 10% or 10 MW (instead of 20% or 40 MW)
  Add a 2 MW minimum; to be a significant decrease the deficiency must be greater than 2 MW

## Slide 45: Modified Significant Decrease Thresholds Examples
CSO | Deficiency | Current Significant Decrease Parameters |  | Proposed Significant Decrease Parameters | 
 |  | Limit (MW) | Significant? | Limit (MW) | Significant?
250.0 | 38.0 | 40.0 | No | 10.0 | Yes
50.0 | 6.3 | 10.0 | No | 5.0 | Yes
25.0 | 3.1 | 5.0 | No | 2.5 | Yes
10.0 | 1.3 | 2.0 | No | 2.0 | No
5.1 | 1.1 | 1.0 | Yes | 2.0 | No
1.1 | 0.231 | 0.220 | Yes | 2.0 | No
The proposed thresholds focus on the larger magnitude deficiencies

## Slide 46: Modified Significant Decrease Thresholds Basis for 2 MW Limit
CSO | Number Observed | Average Total Amount (MW)
< 2 MW | 219 | 104.4
2 – 10 MW | 57 | 249.3
10 – 40 MW | 16 | 295.0
> 40 MW | 3 | 265.4
Total | 295 | 914.1
    Approximately 40% of the 700+ capacity resources each CCP had a CSO less than 2 MW
    - Approx. 280 resources - Average CSO 0.6 MW - Under 175 MW total CSO
    Just over 75% of these resources (nearly 220 each CCP) were deemed to have a ‘significant decrease’
    Over half of these significant decreases were less than 0.3 MW*
    Diminishing returns: the number of resources affected is greater than MWs effected
Table from slide 33
* For context, 0.3 MW is equivalent to the horsepower found in a modest sports car; approximately 400 horsepower 1 Kilowatt = 1.34 Horsepower

## Slide 47: Comparison – Current vs. Proposed
Average each CCP: 708 resources 33,525 MW CSO | Number Observed |  | Average Total Amount | 
 | Current Method | Proposed Method | Current Method | Proposed Method
< 2 MW | 219 | n/a | 104.4 | n/a
2 – 10 MW | 57 | 36 | 249.3 | 156.3
10 – 40 MW | 16 | 11* | 295.0 | 200.9
> 40 MW | 3 | 0 | 265.4 | 0.0
Total | 295 | 47 | 914.1 MW | 357.2 MW
This table compares the current significant decrease determination method to the proposed method using actual deficiencies for the last three ARA3s
    * The proposed method identified some deficiencies as being significant that were not identified using the current method

## Slide 48: Mandatory Demand Bid – MW Amount of Bid
The current process provides for a re-evaluation to determine whether a resource’s deficiency is still a significant decrease
  If partial restoration measures, bilateral transactions or audits, for example, are enough such that a recalculation would then not fail the significant decrease screen, no mandatory demand bid would be used
Under this proposal, the magnitude of the mandatory demand bid would be similar; i.e., a demand bid that is large enough to get the deficiency within the limit

## Slide 49: Mandatory Demand Bids & Significant Decreases Wrap-up
During FCA qualification How much of a CSO in the FCA should you be eligible for, given the capability deficiency the ISO has observed prior to the FCA?
  The proposed significant decrease limits (10% or 10 MW, > 2 MW) will be applied prospectively; FCA 14 at the earliest
During ARA3 qualification Now that you have a CSO, how much of that can you keep given the capability deficiency the ISO has observed prior to ARA3?
  The proposed changes will be phased-in:
    The 2 MW minimum and the modified use of a mandatory demand bid would apply to ARA3 for CCP 11 and all ARA3s thereafter
    The 10% or 10 MW threshold would be applied prospectively; ARA3 for CCP 14

## Slide 50: Annual and Seasonal CSO Bilaterals
What to do with annual and seasonal CSO Bilaterals?

## Slide 51: The Problem with Seasonal CSO Bilaterals
Annual Reconfiguration Transactions ARTs will replace annual CSO Bilaterals
  ARTs do not require any separate processing; ARTs will be done contemporaneously with the ARA
Seasonal and monthly ‘available’ CSO Bilaterals are done using the same process and timing as annual CSO Bilaterals
  The early processing of these CSO Bilaterals (termed ‘available’) allows a participant with a resource abnormality (i.e., a sub-annual problem only) to avoid a situation that would cause a mandatory demand bid to be used in ARA3
Problem: There is no equivalent ART for seasonal CSO Bilaterals

## Slide 52: Seasonal CSO Bilaterals - Issues
There is no seasonal reconfiguration auction
The timing is problematic
Processing seasonal CSO Bilaterals as an ‘annual’ product

## Slide 53: Seasonal CSO Bilaterals - Issue #1
There is no seasonal reconfiguration auction
Issue: Fundamental to the ART construct is an auction clearing price
  Without a seasonal clearing price no seasonal reconfiguration transaction is possible
Seasonal CSO Bilaterals are not standardized
  Seasons are not the same for all resources
  All seasonal CSO Bilaterals must be for a season within the same commitment period, however:
    For some resources June through September is the summer season
    For other resources June through November, April and May is the summer season

## Slide 54: Seasonal CSO Bilaterals - Issue #2
The timing is problematic
Issue: Seasonal and monthly ‘available’ CSO Bilaterals can change the total capacity inside zones between ARA2 and ARA3
  The ‘surplus’ has value (surplus in this context meaning transfers across zone boundaries where substitution is kW-for-kW)
The value of the surplus is inherent in the auction
  E.g., Capacity in an import-constrained zone could be transferred to Rest-of-Pool in an ARA, reducing the total in the zone from a surplus to a point on the zonal MRI curve; in this case, the change in the total capacity within the zone (which includes the surplus) has been valued by participants via their demand bids and supply offers
When done before ARA3 these CSO Bilaterals merely assign the surplus to the first participants to submit seasonal (or monthly) CSO Bilaterals

## Slide 55: Seasonal CSO Bilaterals - Issue #3
Processing seasonal CSO Bilaterals as an ‘annual’ product
Issue: Seasonal CSO Bilaterals, because they are processed before ARA3, are reviewed using the same reliability standards as annual CSO Bilaterals
  But, recall that seasonal CSO Bilaterals were created primarily so that a participant with an abnormality (i.e., a sub-annual problem only) might avoid a mandatory demand bid in ARA3, and that
  This proposal would not require the use of a mandatory demand bid in ARA3 in the case of an abnormality, consequently…
Processing seasonal CSO Bilaterals after ARA3 using the same limits and reliability standards as monthlies renders seasonal CSO Bilaterals the equivalent of an amalgamation of monthly CSO Bilaterals
  ARA3 is conducted in March, June monthlies are processed in April

## Slide 56: Seasonal CSO Bilaterals - Proposal
For the following reasons, the proposal is to phase-out seasonal and monthly ‘available’ CSO Bilaterals along with annual CSO Bilaterals
Creating seasonal auctions would be a major undertaking
  What would be the standard seasons?
Seasonal CSO Bilaterals and monthly ‘available’ bilaterals are not needed to avoid a mandatory demand bid in ARA3
  Mandatory demand bids would not be used in the case of an abnormality
Seasonal CSO Bilaterals would become an amalgamation of opportunities that are already available
  E.g., A summer CSO Bilateral would be the same as submitting four (or eight?) monthly CSO Bilaterals

## Slide 57: conforming changes for annual reconfiguration transactions - A Summary
Monthly CSO Bilaterals and reconfiguration auctions
Significant decrease thresholds and ‘mandatory’ demand bids in ARA3
Annual and Seasonal CSO Bilaterals

## Slide 58: Monthly CSO Bilaterals and Reconfiguration Auctions
Proposal: Use MRI Truncation Points
Beginning with June 2020 (the first month of CCP 11), use the annual MRI-based demand curve truncation point as the zonal fixed requirement for both monthly CSO Bilaterals and reconfiguration auctions
The truncation point being where the zonal MRI-based demand curve price is zero

## Slide 59: Significant Decrease Thresholds and ‘Mandatory’ Demand Bids in ARA3
Proposal:
Modify the ISO’s use of mandatory demand bids such that:
  Their use would not overcorrect in other months; i.e., mandatory demand bids would not be used to address an abnormality
  Their use is consistent with participant allowable limits; a mandatory demand bid would not result in a negative CSO; i.e., base any mandatory demand bid quantity on the least effected month
Modify the significant decrease thresholds used to identify whether or not a monthly deficiency is significant
  Use 10% or 10 MW (instead of 20% or 40 MW)
  Add a 2 MW minimum; to be a significant decrease the deficiency must be greater than 2 MW

## Slide 60: Annual and Seasonal CSO Bilaterals
Proposal:
Phase-out annual, seasonal, and monthly ‘available’ CSO Bilaterals concurrent with the implementation of Annual Reconfiguration Transactions

## Slide 61: Implementation
When can all of this be implemented?

## Slide 62: The Current Situation
At the last meeting (July), the ISO indicated that it would not be able to implement the ART mechanism before the first ARA for Capacity Commitment Period 11 (June 2018)
  The next ARA to use MRI-based demand curves will be ARA1 for CCP 12, which will occur in June 2019
  ARA2 for CCP 11 will occur in August 2019
Since that time, the ISO workload implementing other equally important project changes (e.g., PFP, PRD, CASPR) has increased, possibly further delaying ART implementation

## Slide 63: A Temporary Solution is Needed
The ISO is still evaluating with what confidence it can pledge when the ART proposal can be implemented
However, it is conceivable that the ART solution may not be implemented before it is needed in 2019
  Affecting ARA1 and ARA2 for CCP 11, and ARA1 for CCP 12
Per a participant suggestion at the last meeting, the ISO is evaluating to what degree annual CSO Bilaterals could be used in the interim
Any temporary solution would not, unfortunately, allow for private transactions that could occur in the ARA (i.e., transfers across zonal boundaries when substitution is partial)

## Slide 64: Tariff changes
A preview of the scope of Tariff changes

## Slide 65: Tariff Changes - Sections and Committees
Meeting Date |  |  | 
August | X |  | 
September | X | X | TBD
October | X (vote) | X (vote) | X
November | Participants Committee (vote) |  | 
Tariff Section | Markets Committee | Reliability Committee | Budget & Finance Committee
Section I.2.2 | X | X | X
Section I – Exhibit 1A |  |  | X
Section III.1 | X |  | 
Section III.12 |  | X | 
Section III.13 | X |  | 

## Slide 66: Questions & Comments
A brief response to questions, comments and issues raised at the last stakeholder discussion

## Slide 67: Questions & Comments
Concerns were expressed at the last meeting by a few stakeholders that the ART design may increase customer exposure via increased ARA participation compared to the current CSO Bilateral construct, and requested the Internal Market Monitor to comment.
Is it really necessary to discontinue bilaterals? Can we keep them for trades inside the same zone and across zones when substitution is full?
Would doing CSO Bilaterals as a stop-gap provide bilaterals an advantage over the ARA?
Are CSO Bilaterals really incompatible given the small amount of MWs?
Every MW is important to the participant.
Is there a way to create a price cap for ARTs to limit the price delta?

## Slide 68: Questions & Comments - continued
Concerns were expressed at the last meeting by a few stakeholders that the ART design may increase customer exposure via increased ARA participation compared to the current CSO Bilateral construct, and requested the Internal Market Monitor to comment.
Response: IMM will comment.

## Slide 69: Questions & Comments - continued
Is it really necessary to discontinue bilaterals? Can we keep them for trades inside the same zone and across zones when substitution is full?
Response:
The ART construct provides the same outcome as a CSO Bilateral within the same zone or when substitution is full, while providing more utility and requiring significantly less processing and no separate reliability review.
Using the annual CSO Bilateral construct as a permanent solution would be an inefficient means to allocate the finite capacity transfers possible when capacity is fully substitutable (see the valuation problem discussed regarding seasonal CSO Bilaterals, Issue #2 slide 54).

## Slide 70: Questions & Comments - continued
Would doing CSO Bilaterals as a stop-gap provide bilaterals an advantage over the ARA?
Response:
The temporary ‘advantage’ over the ARA would be the first-come, first-served use of any transfer capability when capacity is fully substitutable across zone boundaries (see the valuation problem discussed regarding seasonal CSO Bilaterals, Issue #2 slide 54).

## Slide 71: Questions & Comments - continued
Are CSO Bilaterals really incompatible given the small amount of MWs?
Response:
Yes. The incompatibility is not a function of how many MW seek to trade as CSO Bilaterals, but rather occurs when the MW being shed and acquired do not have the same reliability benefit (i.e., MRI value).
Under the current rules, CSO Bilaterals are not permitted if they would violate the fixed zonal demand requirements, regardless of the MW involved.

## Slide 72: Questions & Comments - continued
Every MW is important to the participant.
Response:
We agree. Notwithstanding the implementation challenges, ARA1 will provide participants the ability to shed or acquire a CSO.

## Slide 73: Questions & Comments - continued
Is there a way to create a price cap for ARTs to limit the price delta?
Response:
The scope of the ART proposal is, to the extent possible, provide an ‘in-kind’ type of replacement for CSO Bilaterals (i.e., CSO Bilaterals do not have a ‘price-conditional’ functionality).
In the future the ISO could consider suggested enhancements to the ART construct.

## Slide 74: Conclusion

## Slide 75: Conclusion
The problem. The current annual CSO Bilateral construct is incompatible with the use of zonal Marginal Reliability Impact (MRI) demand curves in annual reconfiguration auctions
The proposed solution: Replace annual CSO Bilaterals with Annual Reconfiguration Transactions (ARTs), along with conforming changes

## Slide 76: Stakeholder Schedule
Stakeholder Committee and Date | Scheduled Project Milestone
Markets Committee June 13-14, 2017 | Problem discussion
Markets Committee July 11-12, 2017 | Proposal presentation
Markets Committee August 8-10, 2017 | Proposal and conforming changes discussion
Markets Committee September 12-13, 2017 | Proposal discussion and Tariff language presentation
Markets Committee October 3-4, 2017 | Vote
Participants Committee November 3, 2017 | Vote

## Slide 77
Andrew Gillespie
(413) 540-4088 | Agillespie@iso-ne.com

## Slide 78: Acronyms Used in this Presentation
CSO – Capacity Supply Obligation
MRI – Marginal Reliability Impact
ART – Annual Reconfiguration Transaction - new
CCP – Capacity Commitment Period
ARA – Annual reconfiguration auction
QC – Qualified Capacity
LSR – Local Sourcing Requirement
MCL – Maximum Capacity Limit
PFP – Pay-for-Performance

## Slide 79: Appendix

## Slide 80: Links to Prior Presentations
2017-06-13 and 2017-06-14 MC A07 Zonal Demand Curves: CSO Transactions using MRI Demand Curves
2017-07-11 and 2017-07-12 MC A06 Zonal Demand Curves: CSO Transactions using MRI Demand Curves

## Slide 81: Annual CSO Bilateral & ARA Volume
 | Annual CSO Bilateral 1 | ARA1 | Annual CSO Bilateral 2 | ARA2 | Annual CSO Bilateral 3 | ARA3
CCP 7 | 1.5% | 10.9% | 0.6% | 6.5% | 0.8% | 6.5%
CCP 8 | 0.03% | 4.2% | 0.3% | 10.1% | 0.7% | 9.1%
CCP 9 | 0.05% | 10.3% | 0.1% |  |  | 
CCP 10 | 0.0003% | 9.1% |  |  |  | 
Annual CSO Bilateral – percentage of FCA cleared capacity
ARA – percentage of FCA cleared capacity participating in ARA

## Slide 82: Monthly CSO Bilateral & ARA Volume
Data from Capacity Commitment Periods 1 - 7
Each value is a percentage of FCA cleared capacity
 | Summer Months | Winter Months
Ave. monthly reconfiguration auction |  | 
Participation | 7.3 % | 8.6 %
Cleared | 1.1 % | 1.7 %
Ave. monthly CSO Bilateral |  | 
 | 0.7 % | 0.8 %

## Slide 83: Annual Reconfiguration Auction Schedule and Demand Parameters Used
Jun - May | Capacity Commitment Period | FCA | ARA1 | ARA2 | ARA3 | System Demand Parameter | Zonal Demand Parameter | CSO B/L Parameters/Limits
2017-2018 | CCP8 | Feb '14 | June '15 | Aug '16 | Mar '17 | Fixed (ICR) Fixed (LSR, MCL) |  | Full/no substitution
2018-2019 | CCP9 | Feb '15 | June '16 | Aug '17 | Mar '18 | Sloped linear - continuous | Fixed (LSR, MCL) | Full/no substitution
2019-2020 | CCP10 | Feb '16 | June '17 | Aug '18 | Mar '19 |  |  | 
2020-2021 | CCP11 | Feb '17 | June '18 | Aug '19 | Mar '20 | MRI - continuous |  | Variable substitution
2021-2022 | CCP12 | Feb '18 | June '19 | Aug '20 | Mar '21 |  |  | 
2022-2023 | CCP13 | Feb '19 | June '20 | Aug '21 | Mar '22 |  |  | 

## Slide 84: FCA 11 Results
FCA 11 was held on February 6, 2017
The system cleared 35,835 MW of capacity with a price in Rest-of-Pool of $5.297
SENE cleared 11,736 MW with a congestion price of $0.000
NNE cleared 8,344 MW with a congestion price of $0.000
 | Truncation Point (MW) | Quantity Cleared (MW) | Clearing Price ($/kW-month)
System | n/a | 35,835 | $5.297
SENE | 10,538 | 11,736 | $5.297
NNE | 8,510 | 8,344 | $5.297